## Slide 1: DMR radio
Digital communications

## Slide 2: First thing to do is REGISTER yourself
Think “computer network” … Just as every terminal has own IP address & MAC; Users have logins…
Each person is assigned an unique ID Number
You need to register for user-specific DMR ID
  Go to https://www.radioid.net/cgi-bin/trbo-database/register.cgi
  Select “User Registration” at bottom of page
  Validates callsign using QRZ
  Sends e-mail several hrs later (can be up to 72 hrs)

## Slide 3: DMR “MARC” ID
Registration filed on Internet…
https://www.radioid.net/cgi-bin/trbo-database/
Again, select USER
NAME | CALL | DMR ID
Walter Holmes | K5WH | 1148034
Marty Fitzgerald | W5MF | 1148439
Ron Matusek | WA6TQH | 3148924

## Slide 4: Digital vs. Analog
If you are used to operating on analog FM repeaters, you will have noticed that the audio quality degrades as a station's signal into the repeater (uplink) gets weaker; you start hearing an increase in noise bursts intermixed with the audio until the signal gets too weak that the station can no longer access the repeater or you cannot understand the audio because of noise.
As you move further from the repeater you will start hearing the same noise bursts into your receiver as you the repeater's signal gets weaker (downlink) until you can no longer hear the repeater. A combination of a station's weak signal into a repeater and a repeater's weak signal to the listener can make the usability degrade faster.

## Slide 5: Digital vs. Analog, p2
The basic difference with digital repeaters is that the audio quality remains the same on the uplink and the downlink until the very end of the coverage range; then the audio starts sounding broken (missing portions of the speech) on DMR systems caused by lost packets. The internet can also drop the UDP packets used for moving traffic between repeaters and bridges.
DMR has Forward Error Correction (FEC) which can correct small bit errors, slightly extending the usable range and improving communication quality.

## Slide 6: Types of Digital Radio
D-Star (ICOM / Kenwood / Flex) proprietary AMBE vocoder with Gaussian minimum shift keying or GMSK
  GMSK is a continuous-phase frequency-shift keying modulation scheme
Fusion (Yaesu) AMBE CODEC with C4FM [4-level FS] modulation
DMR utilizes the DSVI AMBE+2™ 3600 bps vocoder by agreement of the manufacturers. Uses TDMA (Time Division) variant of C4FM

## Slide 7: Why DMR?
HAMS adopted Commercial Equipment for repeaters
  Relatively LOW cost
Digital has lower noise / better sound quality
Internet linking lets you access the world
Cheap Chinese Radios

## Slide 8: What is DMR(Digital Mobile Radio)?
A European Telecommunications Standards Institute (ETSI) standard first ratified in 2005.
Meets 12.5kHz channel spacing and 6.25kHz regulatory equivalency standards
Two slot Time Division Multiple Access (TDMA)
4 level FSK modulation
Cutting edge Forward Error Correction (FEC)
Commercial ETSI/TIA specs mean rugged performance and excellent service in RF congested urban environments
Equipment interoperability is certified by the DMR Association

## Slide 9: Basics of DMR – including some lingo
Timeslots
Talkgroups or Digital Contacts
“Color Codes”
Channels
Zones

## Slide 10: Timeslots 2-Slot TDMA
DMR utilizes 2 separate Timeslots, called TS1 and TS2.
Each timeslot is independent from the other meaning both can be used at the same time with no interference from each other.
TS1 is typically Wide-Area, while TS2 is typically more localized.

## Slide 11: (C) TIME SLOTS (TDMA)
Time Division Multiple Access
two logical channels
each 12.5-kilohertz channel space
Separated by 30 ms
http://www.taitradioacademy.com/wp-content/uploads/2014/12/Image-21.png
Radio only monitors 1 or 2 – NOT BOTH

## Slide 12: 2-Slot TDMA
Where the bandwidth of an Analog FM signal is 25.0 kHz, the DMR (TDMA) bandwidth is only 12.5 kHz.
Not only does it occupy half of the required spectrum, but it has the ability to transmit two separate conversations at the same time. This is accomplished by digitally splitting a transmitted signal into alternating 30 millisecond slices referred to as Time Slots.
Reference: Tier II TDMA is the Commercial & Ham Standard TDMA = Time-Division Multiple Access

## Slide 13: Time Slots
Much like a Duplex House, two totally separate families can reside in one structure.
These divisions are referred to as Time Slots.
TS1 TS2
Each house has its own set of rooms. These are referred to as Talk Groups.

## Slide 14: Talk Groups or Digital Contacts
What is a Talk Group or Digital contact ?
Consider it as a conference call in a room
The conference room has the name “AMSAT”
This conference room has only a “phone” connection
In order to connect to the conference you need to dial a number like 98006
So AMSAT=98006, TAC310=310, ect

## Slide 15: Talk Groups or Digital Contacts
Not all repeaters carry all Talk Groups (TG) depending on their network connection, DMR-MARC or Brandmeister. The repeater’s owner or Trustee assigns the TG and TS structure most beneficial for your area. This is to permit the most activity with the least amount of interference.
A typical configuration might be: TG Time Slot
•Local 2 Local Cluster of Repeaters 2 2
•Local 9 Main Repeater Only 9 2
•TAC 310, 311 Secondary Chat Groups 310, 311 2
•Nationwide National Calling Channel 3100 1
•PA State PA Statewide 3142 1
•MD State MD Statewide 3124 1
•Northeast Regional 3172 1

## Slide 16: Talk Groups or Digital Contacts
There are currently over 1200 Talk Groups, ranging from:
- Local Repeater Only
- Local Network Repeaters
- Statewide Groups
- Regional Groups
- Country Specific Groups
- Worldwide Groups
- Specialty Groups Some of the specialty Groups include:
Public Safety - Outdoor Adventure - JOTA (Scouting) - EmComm

## Slide 17: Geographic by Continent  Country
3 1 n xxx
GEORGRAPHIC REGION
N. AMERICA
3-Digit Country Code
United States
(310 or 311)

## Slide 18: (E) TG are Geographic by Continent
0 | TEST NETWORKS | 9 | WORLDWIDE
2xx | EUROPE | 3xx | N. AMERICA & CARRIBEAN
 | 208 = France ; 235 = UK; 262 = Germany |  | 302 = Canada ; 310 = US; 334 = Mexico
4xx | ASIA & MIDDLE EAST | 5xx | OCEANIA
 | 208 = France ; 235 = UK; 262 = Germany |  | 505 = Austrailia ; 310 = US; 334 = Mexico
6xx | AFRICA | 7xx | S. & CENTRAL AMERICA
 | 208 = France ; 235 = UK; 655 = S. Africa |  | 302 = Canada ; 310 = US; 334 = Mexico

## Slide 19: Regional Talkgroup Structure
3175 | S. (Plains) TX + OK
3148 | Texas
3140 | Oklahoma

## Slide 20: TG can get more specific within each region; Some ignore pattern
TG | NAME | COMMENTS
1 / 91 | Worldwide | Any Language
2 | Local/Metro | Common Local Area Metro or Local Repeaters
3 / 93 | North America | United States/Canada (DMR-MARC)
9 | Repeater | Used with SharkRF Openspot
13 | Worldwide English | English Only
9990 | Parrot (Echo) | test
4000 | Disconnect | Used with SharkRF Openspot
5000 | Status (Echo) | Used with SharkRF Openspot

## Slide 21: More Detail (5 & 6 Digit codes)
STATE Sub-Units (5 Digits) , so TX = 3148
  31481 = N Texas; 31482 = S Texas; 31483 = W Texas
REPEATERS – 6 Digits (4 State + 2 ID)
This no longer applies to user ID’s.

## Slide 22: US and Texas Talkgroups
TG | NAME | COMMENTS
310 | TAC 310 | North America Repeater-to-Repeater TG
3100 | DCI Bridge | a general "ragchew talkgroup“ the Bridge has evolved into a worldwide talkgroup since it's cross connection to the Brandmeister platform
3102 | Brandmeister TG | 
3148 | Texas | "Lonestar Talk Group"
3175 | Southern Plains | TX/OK/KS/AR
3185 | Cactus | TX/AZ/CA
8207 | Houston Area Local | Activates all Upper Gulf Coast Repeaters

## Slide 23: Talkgroup – Different Networks
DMR-MARC
  First in USA
  Motorola Repeaters Only
  Subscriber ID Registration
Brandmeister
  Allows Motorola and Hytera Repeaters
  Allows Hotspots
  Some Talkgroups inter-connected
DMR+
  Old Hytera Network

## Slide 24: Talkgroup – Different Networks
Tac310 tg310  LINK  Tac310 tg310
Tac310 tg311  LINK  Tac310 tg311
Tac310 tg312  LINK  Tac310 tg312
DCI/Bridge tg3100  LINK  DCI/Bridge tg3100

## Slide 25: CODEPLUG – Talkgroups or Digital Contacts

## Slide 26: Channels
Channels are a way to define a frequency, timeslot, color code, and talkgroup/contacts
A channel is needed for each talkgroup/contact
If a repeater has 4 talkgroups/contact on each timeslot, it will be necessary to create a total of 8 channels for this repeater.
Remember only 1 talkgroup per timeslot can be used at the same time.

## Slide 27: CODEPLUG – Channels

## Slide 28: Zones
DMR radios support Zones, a Zone is just a grouping of individual channels. Some radio models may limit the number of channels per Zone and the number of Zones allowed.

## Slide 29: CODEPLUG – Zones

## Slide 30: CODEPLUG
A code plug is simply a radio's configuration file.
Using a manufacturer's programming software, you can configure the channels and operating parameters of a radio; this file is then uploaded to the radio.
Building a code plug can take many hours, especially if you want to program hundreds of channels.
The code plug can also contain a Contact List of Radio Ids, call signs, and names to be displayed.
You can find copies of configured code plugs on the internet for different models of radios. Check out the different Yahoo DMR groups.
All DMR radios support a limited number of entries in the contact list.
Starter codeplug : https://dmrtexas.net/code-plugs/

## Slide 31: CODEPLUG CPS (Code Plug Software)

## Slide 32: CODEPLUG – General Settings

## Slide 33: CODEPLUG – Talkgroups or Digital Contacts

## Slide 34: CODEPLUG – Channels

## Slide 35: Channels

## Slide 36: CODEPLUG – Creating Channels

## Slide 37: “Color” Codes
Has nothing to do with color
  Don’t blame me – I didn’t name it
Similar to CTCSS on FM
  Purpose is to filter or ignore other users not using same color code

## Slide 38: “Color” Codes

## Slide 39: CODEPLUG – Zones

## Slide 40: CODEPLUG – Receive Groups
All DMR radios allow you to configure RX Groups.
You can monitor all talkgroups on a single timeslot by adding each Group Contact to an RX Group
Can be used with a dongle like an RF Shark Open Spot to hear messages
Can be confusing. You may rather use scanning in some cases.

## Slide 41: CODEPLUG – Receive Groups

## Slide 42: CODEPLUG – Receive Groups

## Slide 43: CODEPLUG – Scanning
All DMR radios allow you to configure Scan List.
Used on repeaters to scan Talk groups/Digital Contacts
Cannot be used to scan on dongles like DVMega and Openspot

## Slide 44: CODEPLUG – Scanning

## Slide 45: CODEPLUG – Scanning

## Slide 46: CODEPLUG – Software
TYT CPS (Code Plug Software – Difficult to use, unable to sort, and unable to do mass changes.
Code Plug Editor for MD380 by G6AMU v01.15. – Good for sorting lacks documentation
N0GSG DMR Contact Manager 2.60 – Pretty good and work on multiple radios. Cannot sort or insert very easily. Lots of documentation
DL5MCC CPSProgrammer 0.33.0 – Software is a bit rough right now, but should allow you to download a group of repeater from a database online and then push it into your code plug. If this gets finalized it will be the best yet.
RFInder – Hardware/Software/Cell Phone Solution.

## Slide 47: RADIO’s
TYT MD-380 (UHF only), most popular, cheapest, and has TY Toolz firmware to add features for free.
TYT MD-2017 (UHF-VHF), gaining popularity. Track ball.
TYT MD-9600 (UHF-VHF), mobile radio.
TYT MD-uv380 (UHF-VHF). Best yet from TYT
Anytone AT-868uv (UHF-VHF). CPS software is great.
Connect Systems, Hytera, Motorola, Rfinder, and several other off brands available.
Kenwood, Icom, and Yaesu not in DMR yet.

## Slide 48: Talkgroup Usage
Use local TG2 to talk to you buddy down the street
Use area wide like TG8207 Houston area to talk to a group around town
Use state wide like TG3148 Texas Statewide to talk to people in other Texas towns
Use regional like TG3175 South Plains for multiple states.
For even wider, use North America TG3 on DMR-MARC and TG93 Brandmeister
The widest is Worldwide TG1 on DMR-MARC and TG91 Brandmeister
There special talkgroups like TAC310(TG310), DCI Bridge(TG3100), DMR Track (TG31489)

## Slide 49: Talkgroup Usage – Repeater PTT
Repeater owners may implement PTT on certain Talkgroups
Has a time out setting, usually, 10 minutes.
This is so one Talkgroup cannot monopolize a timeslot
To activate, you must key your radio on that Talkgroup. The repeater will remain on that Talkgroup in that timeslot for what ever the time out is set to.

## Slide 50: Promiscuous Mode
DMR repeaters these days carry a number of talkgroups, but those talkgroups are always changing and it can be a pain to constantly update to the latest codeplugs, or to merge codeplugs from multiple repeaters in your region.
MD380Tools comes to the rescue with Promiscuous Mode. Enabling this optional feature will cause your radio to play audio whenever any traffic comes in on your selected timeslot. You can then quickly jot down the settings to update your codeplug.

## Slide 51: DMR-MARC vs Brandmeister Repeaters
DMR-MARC Repeaters have assigned talk groups and time slots per the repeater trustee or administrator.
Brandmeister Repeaters generally do not assign talk groups or time slots.
It is always best to check with your local repeater trustee or administrator.

## Slide 52: Credits and Acknowledgements
John S. Burningham, W2XAB, Amateur Radio Guide to DMR
AE2A DMR BASIC PROGRAMMING
Fred Moore, WD8KNI, fred@fmeco.com – Introduction to DMR
Warren Merkel, KD4Z, hullspeed21@gmail.com – Introduction to DMR
Other unnamed sources.

## Slide 53: Q&A
Questions